## Slide 1: Embedded Systems Design and Implementation GAME: TIC – TAC - TOE
by
Rabert Rajesh Mallavarapu.
14-06-2023, Bolzano.

## Slide 2: Visual Studio Solution
The solution consists of
  Main.cpp
    Where game logic is defined
  Canvas.cpp
    Where functions to create, configure, update and reset a window are declared.
  Canvas.h
    Where global variables and functions are declared.

## Slide 3: Board Setup
RESOLUTION_X = 8
RESOLUTION_Y = 8
Pixels[8][8]
Pad[3][3]

## Slide 4: Player Setup
Player A – Square
  Pixels[xPad][yPad] = 1
  Pixels[xPad+1][yPad] = 1
  Pixels[xPad][yPad+1] = 1
  Pixels[xPad+1][yPad+1] = 1
Player B – Diagonal
  Pixels[xPad][yPad] = 1
  Pixels[xPad+1][yPad+1] = 1

## Slide 5: Move Tile
xPad = {0,3,6}
yPad = {0,3,6}
left = A Pressed
  xPad -= 3
Down = S Pressed
  yPad += 3
Up = W Pressed
  yPad -= 3
Right = D Pressed
  xPad += 3
Enter Pressed = set Tile

## Slide 6: Game Play
Total chances per game = 9
Odd - player one - 5 plays
Even - player two - 4 plays
Check winner after 5 plays
  Winner != 0
    Show winning Sequence
    Show winner
    Show Score Board
Play 5 Games for a tournament

## Slide 7: Game Play
Blink
Show Post

## Slide 8: Winner and ScoreBoard

## Slide 9: Tic-Tac-Toe Circuit on Arduino
Bill Of Materials
 | INPUTS
 | OUTPUTS
Items | Quantity
Buttons | 5
Active Buzzer | 1
Bread Board | 1
Arduino uno | 1
LED Matrix | 1
Red LED | 1
Green LED | 1
Yellow LED | 1
Resistors(250-330 ohms) | 8
optional potentiometer | 1

## Slide 10: Schematic of Circuit for Arduino
Buttons
Left – Up – Right – Down – Enter = {2:6}
LED’s
Red – Green – Yellow = {7-9}
Buzzer = 12
LED Matrix
Clk – CS – DIN = {13, 10, 11}

## Slide 11: Arduino Solution
A typical Arduino solution consists of :
  Variable declaration
  Setup ; one time initialization of functions/variables.
  Loop; the program that is run repeatedly
  Custom Functions.
The Arduino solution rely on the same functions developed in the VS.

## Slide 12: Arduino Solution
The custom functions developed could be divided into three types:
  Initialize and Reset Variables
    InitPixels, InitPad, Boardinit, Gameinit.
  Read variables and update Game
    UpdatePixels, buttonDebug, DrawPad, CheckPad, Blink, CheckWinner, ScoreKepper.
  Display game results
    showPost, ShowWinner, ShowScore, ShowCredits.

## Slide 13: Custom Functions
UpdatePixels
Sets pixel of the ON/OFF using mx.setpoint( x, y, 0/1)
A variation UpdateIntensity takes input (0-1) to set brightness of the pixels.
ButtonDebug
Sets the Yellow LED and Buzzer to HIGH if any button is HIGH.
ShowCredits
Uses Md.Parola to write a message to the led matrix, e.g.: “Winner – A – New Game ? “

## Slide 14: Video Presentation

## Slide 15: THE END
THANK YOU !
QUESTIONS ?